## Slide 1: Monitoring - network traffic – on the terminal side
Gábor Fehér, Balázs Lajtha – Budapest University of Technology and Economics

## Slide 2: Outline
Monitoring
Terminal side traffic monitoring scenarios
Android capabilities for monitoring
The application
Firewall solution
VPN solution
Summary and future work

## Slide 3: Monitoring
Data helping to improve QoE and detect white spots
  User device
  Used applications
  Running services
  Location and speed
  User network technology
  Packet level network traffic data

## Slide 4: Monitoring scenarios – for the provider
Know more
  About your customer
    What devices do customers use
    What applications does customers use
    When do they use it
    Where do they use it
  About your service
    What quality do you provide at the endpoint
Remote assistance

## Slide 5: Monitoring scenarios – for the user
Self diagnostics
  Check how your network performs without active synthetic measurements
  Check if app performance is related to a network issue
  Provide proof of network defects
Malware detection
  With the proper analysis tools detect misbehaving applications

## Slide 6: Android capabilities

## Slide 7: Android capabilities – network traffic
Linux
  tcpdump
  Firewall rules
Apps
  tPacketCapture
API
  TrafficStats – since 2.2
    Total/cellular traffic
    Traffic by userId
    Traffic by protocol (TCP vs UDP)
  VPNService – since 4.0

## Slide 8: The application
Features
  Collected data
    Running applications and services
    Foreground application and activity
    Battery level and charging state
    CPU and memory usage
    Easy to extend through Task interface
  Data polled periodically
    Polling each second doesn’t drain battery
  File format
    Each Task has it’s own output file, string log message required
  Data collection
    Data is uploaded periodically to a server through selected network protocol and SSID

## Slide 9: The application – user interface
Notification – required by the platform
Main screen – system log, start/stop monitoring, tagging
Settings – server and credentials, timing, network

## Slide 10: The firewall solution
Linux tools
  Uses firewall rules to capture packets
  Find applications when TCP syn packet found
  softflowD counts data volume and packets
Flow data is saved with application id
Requires root access

## Slide 11: VPN solution
Since 4.0
Needs user’s permission to create VPN interface
Doesn’t require root access
Intended for VPN purposes

## Slide 12: The VPN solution – technical details
Raw IP packets sent through the tunnel interface can be read from an InputStream
Raw IP packets are expected by an OutputStream
Normal operation
  Open a socket, exclude socket from VPN
  Read data from InputStream
  Send data through the socket to a VPN server
  Receive data on the socket
  Write received data to the tunnel’s stream
Sniffer operation
  Sending and receiving of raw IP packets is a root protected feature
  Have to use high level sockets to send out and receive data

## Slide 13: The VPN solution –operation
Receive data from InputStream
Find packets
Extract IP and transport headers from packets
Create the appropriate sockets
Send data
Receive data
Build raw headers for received data
Write packets to OutputStream

## Slide 14: The VPN solution – issues
Managing sockets
  Timeout parameters, window size
Implementing TCP signaling
  Sequence numbers, acknowledgments, SYN message flow is required in the raw IP packets but is not accessible from the TCP sockets
Packet information is lost for TCP
  No incoming packets: no timing no packet length, only stream
Synchronization
Performance
  Not measured yet

## Slide 15: Current state
The application
  Ready
  Minor modifications needed in the upload procedure
The softflow based solution
  Ready
  Tested and ran on several devices
  Overall a couple of month worth of traffic data collected
VPN solution
  UDP in prototype phase
  TCP solution under development
  Testing infrastructure under development

## Slide 16: Future work
Finish and deploy VPN based solution
Process data
  Use data as training set for flow based application authentication
  Perform controlled experiments to generate flows with known quality of experience for some applications

## Slide 17: www.hsnlab.hu hsnlab.tmit.bme.hu
Thank you!
Questions?